## Slide 1: Understanding Geolocation Accuracy using Network Geometry Brian Eriksson Technicolor Palo Alto
Mark Crovella
Boston University

## Slide 2
Our focus is on IP Geolocation
Target
Internet
?
?
?
?
?
Geographic location (geolocation)?
Why? : Targeted advertisement, product delivery, law enforcement, counter-terrorism

## Slide 3: Measurement-Based Geolocation
(known location)
1
  Known geographic location
Landmark
(unknown location)
delay
Target
  Delay Measurements to Targets
2
  Landmark Properties:
d
Estimated Distance
-Estimated distance (Speed of light in fiber)

## Slide 4: Measured Delay vs. Geographic Distance
Measured Delay (in ms)
Geographic Distance (miles)
Over 80,000 pairwise delay measurements with known geographic line-of-sight distance.
Ideal

## Slide 5
Measured Delay (in ms)
Geographic Distance (miles)
Why does this deviation occur?
Sprint North America
Delay-to-Geographic Distance Bias
Landmark
Target
Line-of-sight
Routing Path
The Network Geometry (the geographic node and link placement of the network) makes geolocation difficult

## Slide 6: To defeat the Network Geometry, many measurement-based techniques have been introduced.
Methodology | Published Median Error
Shortest Ping - [Katz -Bassett et. al. 2007] | 69 miles
Topology-Based - [Katz -Bassett et. al. 2007] | 118 miles
 | 41 miles
Constraint-Based – [Gueye et. al. 2006] | 13.6 miles
 | 59 miles
Posit – [Eriksson et. al. 2012] | 21 miles
Street-Level - [Wang et. al. 2011] | 0.42 miles
Best Technique
Worst Technique
?
?
All of these results are on different data sets!

## Slide 7: The number of landmarks is inconsistent.
Methodology | Published Median Error | Number of Landmarks
Shortest Ping - [Katz -Bassett et. al. 2007] | 69 miles | 68
Topology-Based - [Katz -Bassett et. al. 2007] | 118 miles | 11
 | 41 miles | 68
Constraint-Based – [Gueye et. al. 2006] | 13.6 miles | 42
 | 59 miles | 95
Posit – [Eriksson et. al. 2012] | 21 miles | 25
Street-Level - [Wang et. al. 2011] | 0.42 miles | 76,000
What if this technique used 76,000 landmarks?
What if this technique used 11 landmarks?

## Slide 8: And, the locations are inconsistent.
Methodology | Published Median Error | Number of Landmarks | Locations
Shortest Ping - [Katz -Bassett et. al. 2007] | 69 miles | 68 | North America
Topology-Based - [Katz -Bassett et. al. 2007] | 118 miles | 11 | North America
 | 41 miles | 68 | North America
Constraint-Based – [Gueye et. al. 2006] | 13.6 miles | 42 | Western Europe
 | 59 miles | 95 | Continental US
Posit – [Eriksson et. al. 2012] | 21 miles | 25 | Continental US
Street-Level - [Wang et. al. 2011] | 0.42 miles | 76,000 | United States

## Slide 9: Our focus is on characterizing geolocation performance.
vs.
1
How does accuracy change with the number of landmarks?
2
How does accuracy change with the geographic region of the network?
vs.
“Poor” Geolocation Performance
“Excellent” Geolocation Performance
3 landmarks
10 landmarks

## Slide 10: We focus on two methods:
Methodology | Published Median Error | Number of Landmarks | Locations
Shortest Ping - [Katz -Bassett et. al. 2007] | 69 miles | 68 | North America
Topology-Based - [Katz -Bassett et. al. 2007] | 118 miles | 11 | North America
 | 41 miles | 68 | North America
Constraint-Based – [Gueye et. al. 2006] | 13.6 miles | 42 | Western Europe
 | 59 miles | 95 | Continental US
Posit – [Eriksson et. al. 2012] | 21 miles | 25 | Continental US
Street-Level - [Wang et. al. 2011] | 0.42 miles | 76,000 | United States

## Slide 11
Constraint-Based
Target
Landmarks

## Slide 12
Feasible Region
Constraint-Based
Maximum Geographic Distance

## Slide 13
Constraint-Based
Estimated Location
Feasible Region Intersection

## Slide 14
Constraint-Based
Estimated Location
Feasible Region Intersection
Shortest Ping
Target
Landmarks
Estimated Location
Smallest Delay

## Slide 15
Shortest Ping w/ 6 landmarks
Shortest Ping w/ 5 landmarks
Background: Fractal dimension, Hausdorff dimension, covering dimension, box counting dimension, etc.
Maximum Geolocation Error
Maximum Geolocation Error
Shortest Ping w/ 4 landmarks
Where the Network Geometry defines the scaling dimension, β>0
α error (-β)
Number of Landmarks
Maximum Geolocation Error

## Slide 16
Given shortest path distances on network geometry, we use ClusterDimension [Eriksson and Crovella, 2012]
Intuition: Measures closeness of routing paths to line of sight.
Scaling dimension, β = 1.119
β = 0.557
β = 0.739
Estimated scaling dimension, β
Network Geometry

## Slide 17: Scaling Dimension and Accuracy
error α M(-1/β)
For M landmarks and scaling dimension β, we find:
β = 0.557
Large reduction in error using more landmarks.
β = 1.119
Small reduction in error using more landmarks.
M α error (-β)

## Slide 18
(M)
Ring Graph
(dim. β ≈ 1)
Grid Graph
(dim. β ≈ 2)
2
Both graphs follow a power law decay (γ) with respect to geolocation error rate.
1
The intuition holds, the accuracy decays like O(M- 1/β)
Higher dimension networks perform better with few landmarks
Lower dimension networks perform better with many landmarks
Power Law Decay = -γring
Power Law Decay = -γgrid

## Slide 19: Topology Zoo Experiments
Internet Topology Zoo Project - http://www.topology-zoo.org/
Region | Number of Networks
Europe | 7
North America | 8
South America | 3
Japan | 2
Oceania | 4
1
From network geometry - Estimated Scaling Dimension, β
2
Geolocation error power law decay, γ (assumption, ≈ 1/β)

## Slide 20
R2 = 0.855
R2 = 0.787
Shortest Ping and Scaling Dimension
Constraint-Based and Scaling Dimension
Goodness-of-fit to 1/β curve
γ
β

## Slide 21: We find consistency across geographic regions.
Geographic Region | Number of Networks | Scaling Dimension | 
 |  | Mean | Standard Dev.
Japan | 2 | 1.104 | 0.083
Europe | 7 | 1.148 | 0.32
North Amer. | 8 | 0.924 | 0.223
South Amer. | 3 | 0.681 | 0.053
Oceania | 4 | 0.617 | 0.069
“Poor” Geolocation Performance
“Excellent” Geolocation Performance

## Slide 22: Conclusions
Geolocation accuracy comparison is difficult due to inconsistent experiments.
Methodology | Published Median Error | Number of Landmarks | Locations
Shortest Ping - [Katz -Bassett et. al. 2007] | 69 miles | 68 | North America
Topology-Based - [Katz -Bassett et. al. 2007] | 118 miles | 11 | North America
 | 41 miles | 68 | North America
Constraint-Based – [Gueye et. al. 2006] | 13.6 miles | 42 | Western Europe
 | 59 miles | 95 | Continental US
Posit – [Eriksson et. al. 2012] | 21 miles | 25 | Continental US
Street-Level - [Wang et. al. 2011] | 0.42 miles | 76,000 | United States

## Slide 23: Conclusions
The scaling dimension of a network is proportional to its geolocation accuracy decay.
Ring Graph
(dimension ≈ 1)
Grid Graph
(dimension ≈ 2)

## Slide 24
Results on real-world networks fit to this trend and demonstrate consistency across geographic regions.
R2 = 0.855
Conclusions
Geographic Region | Number of Networks | Average Scaling Dimension
Japan | 2 | 1.104
Europe | 7 | 1.148
North America | 8 | 0.924
South America | 3 | 0.681
Oceania | 4 | 0.617

## Slide 25
Questions?