## Slide 1: AliasCluster: A Lightweight Approach to Interface Disambiguation Brian Eriksson Technicolor Palo Alto
Larissa Spinelli
Mark Crovella
Boston University

## Slide 2: Map of the Internet?
www.lumeta.com
Maps are limited by the measurement tool used : Traceroute.
Traceroute Limitations:
  Limited probing coverage
  Network Load
  Anonymous Routers
Main Focus: Interface IPs ≠ Physical Routers

## Slide 3
Consider three Traceroute paths:
Prior work (Marchetta et. al. 2011) has shown 10x more interfaces than physical routers
A → D → F
B → E → G
C → E → H
Inferred topology from Traceroute:
Possible True Physical Topology:
Router #1
Router #2
Router #3
Goal: Interface Disambiguation – Determining aliases : which interface IPs belong to the same physical router.

## Slide 4: Prior Disambiguation Work and Limitations
Rocketfuel (Ally) – Spring et. al. 2002
Mercator (Iffinder) – Govindam et. al. 2000
Prespecified Timestamps – Sherry et. al. 2010
Merlin – Marchetta et. al. 2011
MIDAR – Keys et. al. 2011
Radargun – Bender et. al. 2008
DisCarte – Sherwood et. al. 2008
APAR (Kapar) – Gunes et. al. 2008
Can we estimate router aliases from Traceroute measurements only?
Requires Additional Probing
Requires Router Specific Options
Traceroute Only

## Slide 5
In this paper, we introduce AliasCluster
A and E aliased?
B and H aliased?
2
Given pairwise likelihoods, can we infer router clusters?
1
Given interface IP pairs, how likely is it that they belong to the same physical router?
A → D → F
B → E → G
C → E → H
Given Traceroute Paths:
A
B
C
D
E
F
G
H
Router 1
Router 2
Router 3
A and C aliased?
A and E aliased?
B and C aliased?
C and D aliased?
D and E aliased?
D and H aliased?
F and G aliased?
G and H aliased?

## Slide 6
Consider two observed IP interfaces, i and j.
Given interface IP pairs, how likely is it that they belong to the same physical router?
1
Goal:
Set of relevant features of i and j from Traceroute.
For example, IP Subnet
  Likely that 173.194.40.84 and 173.194.40.86 (e.g., /30) are aliases
  Less likely that 173.194.40.84 and 173.92.9.185 (e.g., /8) are aliases

## Slide 7
Key observation - Down-path observations contain relevant alias information
  Percentage Out-degree Match
    Out of all the down-path interfaces observed for interface A, what percent are observed for both A and B?
  Percent Hop Count Match
    For those commonly observed interfaces, what percent observe the same hop count?
Aliases
A
B
Non-Aliases
B
A
X
Common out-degree interface
X
Unique out-degree interface
A → … → X
B → … → X
A→M→N→X
B→P→Q→X
2 hops

## Slide 8
IP Subnet
Hop Match Percent
Out-Degree Match Percent

## Slide 9
Given interface IP pairs, how likely is it that they belong to the same physical router?
1
Traceroute extracted features (e.g., IP subnet, hop count match,etc.)
Solution: Naïve Bayes (i.e., assume independence)
Transforms problem from estimating one K-dimension likelihood, to estimating K one-dimensional likelihoods.

## Slide 10: Naïve Bayes – Combined Performance

## Slide 11
Consider the following problem with 3 IP interfaces:
While Naïve Bayes is returns the likelihood that two interfaces are aliased, not the inferred routers clusters.
i
j
k
is high
is high
is low
What is the physical router?
i,j?
i,k?
i,j,k?
2
Given pairwise likelihoods, can we infer router clusters?

## Slide 12
2
Given pairwise likelihoods, can we infer router clusters?
i
j
Alias Likelihood Matrix
We perform a modified hierarchical clustering approach.

## Slide 13
2
Given pairwise likelihoods, can we infer router clusters?
Alias Likelihood Matrix
We perform a modified hierarchical clustering approach.
N Interfaces
N Interfaces

## Slide 14
2
Given pairwise likelihoods, can we infer router clusters?
Alias Likelihood Matrix
Largest Likelihood, s1
m
n
m
n
s1
We perform a modified hierarchical clustering approach.

## Slide 15
2
Given pairwise likelihoods, can we infer router clusters?
Alias Likelihood Matrix
2nd Largest Likelihood, s2
y
x
m
n
s2
x
y
0
s1
We perform a modified hierarchical clustering approach.

## Slide 16
We perform a modified hierarchical clustering approach.
2
Given pairwise likelihoods, can we infer router clusters?
Alias Likelihood Matrix
s2
s1
Repeated until the tree is found
s3
s4
s5
s6
s7

## Slide 17
Using the internal node values, we threshold to resolve physical routers.
  Consider S1 > S2 > S3 > S4 > S5 > S6 > S7
The detection/false alarm rate as this threshold is adjusted defines the performance of AliasCluster.
S4 > λA > S5
S5 > λB > S6

## Slide 18: Experiment Setup
Traceroute data is from the CAIDA Macroscopic Internet Topology Data Kit from July 2010
  54 source monitors to all /24 prefixes
  Over 2.1 million unique router interface addresses
Ground truth router aliases found using the MERLIN project (Marchetta et. al. 2011).
  Allow us to consider subset of routers with true positives and true negatives.
This reduces the topology under consideration to 63,479 router interfaces in 19,027 physical routers.

## Slide 19
Methodology | Number of False Alarms | Percentage of False Alarms (x10-5)
KAPAR (Keys 2012) | 16,644 | 3.305
AliasCluster | 8,388 | 1.666
For KAPAR’s 26% detection rate on the ARK measurements:
Methodology | 20% Detection Rate | 30% Detection Rate | 40% Detection Rate
AliasCluster | 7.92 x 10-6 | 1.26 x 10-4 | 7.58 x 10-4
False alarm rates for varying detection rates:

## Slide 20: Conclusions
AliasCluster – A lightweight technique for interface disambiguation
  Requires no additional probes/measurements
  Using statistical learning to determine aliases from Traceroute only
  General framework allows for extensions to other features
Experiments on CAIDA Ark measurements results in 50% reduction in the false alarm rate compared with the current state-of-the-art.

## Slide 21: Future Work
Larger-scale studies
  Aggregated Ark Trace data sets
  More alias ground truth information
Additional Traceroute extracted features
Historical longitudinal study
  How has the number of routers changed over time?

## Slide 22: Questions?

## Slide 23
Given interface IP pairs, how likely is it that they belong to the same physical router?
1
Traceroute extracted features (e.g., IP subnet, common down-path interfaces,etc.)
Why difficult? – The “curse of dimensionality”
Solution: Naïve Bayes (i.e., assume independence)
Transforms problem from estimating one K-dimension likelihood, to estimating K one-dimensional likelihoods.
Prior term – Easy to calculate
Likelihood term – Difficult to calculate